## Slide 1: Overview of MODFLOW 6 Newest capabilities & ongoing developments

## Slide 2: MODFLOW 6 Objectives
Provide a single program that consolidates simulation capabilities in the numerous MODFLOW variants, including, for example:
  MODFLOW-2005
  MODFLOW-LGR
  MODFLOW-NWT
  MODFLOW-USG
  SEAWAT
  GSFLOW
Support multiple model instances and multiple model types in a single simulation
Provide a platform for extending MODFLOW into a configurable hydrologic simulator

## Slide 3: Range of Scales for MODFLOW Applications
bench
site
subregional
regional
national
global

## Slide 4: MODFLOW 6 Components
Simulation
Solution Types
  Implicit
  Explicit
Model Types
  Groundwater Flow (GWF)
  Groundwater Solute Transport (GWT)
  Groundwater Energy Transport (GWE)
  Particle Tracking (PRT)
In development
  Overland Flow (OLF)
  Channel Flow (CHF)
Solutions
Models
Timing
Exchanges
Packages

## Slide 5: Temporal Discretization
Stress periods, Time steps
Equidistant, or TSMULT
Adaptive time stepping (ATS)
Reduced when solver fails, or
Get maximum dt from Models
ATS input:
ADV input:

## Slide 6: Spatial Discretization
Rectilinear – Discretization DIS
Unstructured – Discretization by Vertices DISV (layered)
Unstructured – Discretization by Connections DISU (prismatic)

## Slide 7: Groundwater Flow (GWF) Model
Highlights
  Newton or standard formulation
  Full 3D anisotropy (XT3D)
  Compaction and subsidence (CSUB)
  Multiple stress packages of the same type
  Advanced stress packages (SFR, LAK, MAW, UZF)
  Water mover (MVR)

## Slide 8: Groundwater Transport (GWT) Model
Highlights
  Advection, dispersion, sorption, decay/growth
  Mobile and immobile domains
  Advanced packages (SFT, LKT, MWT, UZT)
  Water mover for transport (MVT)

## Slide 9: Groundwater Energy (GWE) Transport Model
Heat-transport equivalents a thing of the past!
Facilitates smoother parameter estimation investigations
GWE more readily supports
  Geothermal investigations
  Ecological investigations
  Better leveraging of inexpensive temperature observations for improved calibration of a GWF model

## Slide 10: Groundwater Energy (GWE) Transport Model
GWF + GWE + PRT
Barends, F.B.J. 2010. Complete Solution for Transient Heat Transport in Porous Media Following Lauwerier's Concept. Society of Petroleum Engineers Annual Technical Conference and Exhibition, Florence, Italy. SPE-134670-MS https://doi.org/10.2118/134670-MS.

## Slide 11: Exchanges
Communication between any two models occurs through an ”exchange”
Exchange types:
  GWF-GWF: connects two GWF Models
  GWT-GWT: connects two GWT Models
  GWE-GWE: connects two GWE Models
  GWF-GWT: provides the simulated flows from a GWF Model to a GWT Model
  GWF-GWE: provides the simulated flows from a GWF Model to a GWE Model
MODEL
MODEL
EXCHANGE

## Slide 12: Solutions
Dependent variables for one or more models are calculated by a “solution”
A focus of MODFLOW 6 has been on the Iterative Model Solution (IMS)
IMS solves for head (GWF), concentration (GWT), temperature (GWE)
Explicit Model Solution (EMS) introduced for particle tracking (PRT)
MODEL
MODEL
EXCHANGE
SOLUTION

## Slide 13: Exchange Data
Connect two GWF models by specifying a GWF-GWF Exchange in the configuration
Exchange file contains geometrical data for connection between neighboring nodes
Ln
n
m
Lm
Δw
Model 1
Model 2
Notes: A user can couple two GWF models by specifying a GWF-GWF exchange. The exchange file contains geometrical data for how cells are connected across models.

## Slide 14: Generalized Control-Volume Finite-Difference Numerical Solutions

## Slide 15: Single-Model Configurations
Simulation
Numerical Solution
Groundwater Flow Model
Temporal Discretization
Simulation
Numerical Solution
Groundwater Transport Model
Temporal Discretization

## Slide 16: Multi-Model Configurations
Simulation
Numerical Solution
Groundwater Flow Model 1
Temporal Discretization
Groundwater Flow Model 2
GWF-GWF Numerical Exchange
Simulation
Numerical Solution 1
Groundwater Flow Model
Temporal Discretization
Groundwater Transport Model
GWF-GWT Exchange
Numerical Solution 2

## Slide 17: Multi-Model Configurations
Simulation
Numerical Solution 1
Groundwater Flow Model 1
Temporal Discretization
Groundwater Flow Model 2
GWF-GWF Numerical Exchange
Numerical Solution 2
Groundwater Transport Model 1
Groundwater Transport Model 2
GWT-GWT Numerical Exchange
GWF-GWT
Exchange 1
GWF-GWT
Exchange 2

## Slide 19: Parallel Computing
Large national/continental scale models
High resolution, regional models
Targeting HPC as well as laptops
Model of a Regional Groundwater Basin in Southern California,
Tetra Tech 2023
Runtimes:
1* core: > 250 hrs
250 cores: 1.7 hrs

## Slide 20: Parallel Computing: density dependent
Flow_1
Flow_2
Flow_3
Flow_4
Trans_1
Trans_2
Trans_4
Trans_3
Flow
Trans
Serial Simulation
Parallel Simulation

## Slide 21: Salt Lake
Coupled variable-density flow and solute transport simulation
Experimental Hele-Shaw Cell Study of Wooding et al.
From the “MODFLOW 6 Examples”:

## Slide 22: Parallel Salt Lake in 3 dimensions
GHB

## Slide 23: Unsaturated Zone: 3D Richards
s
z
UZR
N
NPF
N
dry
MODFLOW 6: confined and unconfined groundwater
NPF: saturated fraction SF (which is not saturation)

## Slide 24: UZR package
Integration with NPF based on the premise that
Richards Equation for variably saturated conditions, smoothly becomes standard NPF flow equation when fully saturated
Very similar to MODFLOW-USG
Benefits
  Apply Richards Eq. only when unsaturated
  Works with Transport, PRT
  Multi-model and Parallelization supported
  Newton option
  Adaptive Timestepping

## Slide 25: Unsaturated Zone: Keating Problem
Water table problem with perched aquifer
Unconfined flow and solute transfer in MODFLOW 6 through “dry” cells with ‘Newton’ option

## Slide 26: Unsaturated Zone: Keating Problem
First 3D Richards simulation with the UZR package:

## Slide 27: Channel and Overland Flow Models
Two new surface water flow models are under development
  Channel Flow (CHF) Model
  Overland Flow (OLF) Model
These are not GWF “packages”; they are separate “models” with their own discretization and packages
The models will run by themselves or coupled with another model

## Slide 28: Motivators
MOD-HMS
SWR Process for MODFLOW

## Slide 29: Diffusion Wave Model
One-dimensional channel flow
Two-dimensional overland flow
Manning’s equation

## Slide 30: Channel Flow (CHF) Model Discretization
Discretization by Vertices in 1D (DISV1D)

## Slide 31: Overland Flow (OLF) Model Discretization
Discretization by Vertices in 2D (DISV2D)
Structured Grid in 2D (DIS2D)

## Slide 32: Channel Cross Section (CXS) Package

## Slide 33: Surface-Water Benchmarks

## Slide 34: Delaware River Basin
MODFLOW

## Slide 35: Channel Flow (CHF) Simulation

## Slide 36: MODFLOW 6 Timeline
2013 – Initiated development
2017 – First release with the Groundwater Flow (GWF) Model
2020 – MODFLOW Application Programming Interface (API)
2020 – Release of Groundwater Transport (GWT) Model
2023 – Release of parallel simulation capabilities
2024 – PRT, GWE, NetCDF
2025/26 – Richards, Surface Water, …